# Building LibreOffice on a MacPro with OS X 10.6.4

1. Installed 10.6.4
2. Software Update - installed all updates.
3. Installed xCode 3.2.4 w/10.4 SDK
4. Installed GIT 1.7.3.1 (Git - Fast Version Control System)
5. Install libgmp (The GNU MP Bignum Library)
./configure
make
sudo make install
# the above built the 64bit version; now we need the 32bit version
<delete the project directory>
<restore a new copy of the project>
export ABI=32
./configure
make
cd .libs
lipo -create libgmp.10.dylib /usr/local/lib/libgmp.10.dylib -output libgmp.10.dylibf
sudo mv libgmp.10.dylibf /usr/local/lib/libgmp.10.dylib
lipo -create libgmp.a /usr/local/lib/libgmp.a -output libgmp.af
sudo mv libgmp.af /usr/local/lib/libgmp.a

Install coreutils (Index of /gnu/coreutils)
./configure CC="gcc -arch i386 -arch x86_64" CXX="g++ -arch i386 -arch x86_64" CPP="gcc -E" CXXCPP="g++ -E" --program-prefix=g
make
sudo make install

Install pkg-config (pkg-config Wiki – FrontPage)
./configure CC="gcc -arch i386 -arch x86_64" CXX="g++ -arch i386 -arch x86_64" CPP="gcc -E" CXXCPP="g++ -E"
make
sudo make install

Install gettext (gettext - GNU Project - Free Software Foundation (FSF))
./configure CC="gcc -arch i386 -arch x86_64" CXX="g++ -arch i386 -arch x86_64" CPP="gcc -E" CXXCPP="g++ -E"
make
sudo make install
Install M4 (Index of /gnu/m4)
./configure CC="gcc -arch i386 -arch x86_64" CXX="g++ -arch i386 -arch x86_64" CPP="gcc -E" CXXCPP="g++ -E"
make
sudo make install

Install autoconf (Index of /gnu/autoconf)
./configure CC="gcc -arch i386 -arch x86_64" CXX="g++ -arch i386 -arch x86_64" CPP="gcc -E" CXXCPP="g++ -E"
make
sudo make install

Install automake (Index of /gnu/automake)
./configure CC="gcc -arch i386 -arch x86_64" CXX="g++ -arch i386 -arch x86_64" CPP="gcc -E" CXXCPP="g++ -E"
make
sudo make install

1. Install libiconv (libiconv - GNU Project - Free Software Foundation (FSF))
  1. I had issues getting glib2 to use the base version
./configure CC="gcc -arch i386 -arch x86_64" CXX="g++ -arch i386 -arch x86_64" CPP="gcc -E" CXXCPP="g++ -E"
make
sudo make install

Install glib2 (ftp.gnome.org)
./configure --with-libiconv=native
Remove %error lines related to libiconv from glib/gconvert.c
make
sudo make install
make clean
./configure CC="gcc -arch i386" CXX="g++ -arch i386" CPP="gcc -E" CXXCPP="g++ -E" --with-libiconv=native
make
lipo -create gio/.libs/libgio-2.0.0.dylib /usr/local/lib/libgio-2.0.0.dylib -output libgio-2.0.0.dylib
lipo -create glib/.libs/libglib-2.0.0.dylib /usr/local/lib/libglib-2.0.0.dylib -output libglib-2.0.0.dylib
lipo -create gmodule/.libs/libgmodule-2.0.0.dylib /usr/local/lib/libgmodule-2.0.0.dylib -output libgmodule-2.0.0.dylib
lipo -create gobject/.libs/libgobject-2.0.0.dylib /usr/local/lib/libgobject-2.0.0.dylib -output libgobject-2.0.0.dylib
lipo -create gthread/.libs/libgthread-2.0.0.dylib /usr/local/lib/libgthread-2.0.0.dylib -output libgthread-2.0.0.dylib
sudo mv libgio-2.0.0.dylib /usr/local/lib/libgio-2.0.0.dylib
sudo mv libglib-2.0.0.dylib /usr/local/lib/libglib-2.0.0.dylib
sudo mv libgmodule-2.0.0.dylib /usr/local/lib/libgmodule-2.0.0.dylib
sudo mv libgobject-2.0.0.dylib /usr/local/lib/libgobject-2.0.0.dylib
sudo mv libgthread-2.0.0.dylib /usr/local/lib/libgthread-2.0.0.dylib

Install libIDL (Index of /pub/gnome/sources/libIDL/0.8)
./configure
make
sudo makeinstall
./configure CC="gcc -arch i386" CXX="g++ -arch i386" CPP="gcc -E" CXXCPP="g++ -E"
make
lipo -create .libs/libIDL-2.0.dylib /usr/local/lib/libIDL-2.0.dylib -output libIDL-2.0.dylib
lipo -create .libs/libIDL-2.a /usr/local/lib/libIDL-2.a -output libIDL-2.a
sudo mv libIDL-2.0.dylib /usr/local/lib/libIDL-2.0.dylib
sudo mv libIDL-2.a /usr/local/lib/libIDL-2.a

Install libhunspell (Hunspell: open source spell checking, stemming, morphological analysis and generation under GPL, LGPL or MPL licenses)
./configure CC="gcc -arch i386 -arch x86_64" CXX="g++ -arch i386 -arch x86_64" CPP="gcc -E" CXXCPP="g++ -E"
make
sudo make install

1. git clone git://anongit.freedesktop.org/git/libreoffice/build
2. cd build
3. ./autogen.sh --with-distro=LibreOfficeMacOSX --with-git --with-num-cpus=8 --with-system-hunspell
4. ./download
5. edit /build/libreoffice-3.2.99.2/solver/330/unxmacxi.pro/bin/setup_osl.ins
-> You need to remark out the section of code dealing with libjpipe. It should look like the following:

#File gid_File_Dl_Jpipe
#	Dir = gid_Dir_Ure_Lib;
#	Name = "libjpipe.jnilib";
#	Styles = (PACKED,VERSION_INDEPENDENT_COMP_ID);
#	UnixRights = 444;
#End

1. make
2. sudo make install
-> This will fail with "Failed to generate package file lists"; but it runs anyways.

open /usr/lib/ooo-3.3/LibreOffice.app