## Slide 1: AMD DSC REQUIREMENTS & POLICIES
Presented by Wenjing Liu
for DisplayPort SST/MST

## Slide 2: DSC TERMINOLOGIES

## Slide 3: Target Bpp
DSC achieves video signal compression by reducing amount of bits to represent each pixel (TargetBpp) while keeping the same pixel clock
The compressed bandwidth can be represent by below formula:
Higher TargetBpp will result in higher image quality, but also requires a higher bandwidth in order to drive the timing
TargetBpp is determined by Display Driver based on display capability, link bandwidth and timing
TargetBpp needs to be within the range between 8 bpp – 16 bpp
TargetBpp can be fractional value with minimum step of 1/16 bpp

## Slide 4: DSC Slice
Each slice is an group of DSC pixels compressed together
Horizontal slice count is the number of columns in the grid
Vertical slice count is number of rows in the grid
Each column of slices will use single slide decoder
Slice height represents amount of lines a slice encoder needs to take into account for compression
Pixels |  | 
Slice |  | 
DSC
Video Frame before Compression
Compressed Video Frame
8K60Hz with ~81 Gbps bandwidth
8K60hz with 32.4 Gbps bandwidth

## Slide 5: Picture Parameter Set (PPS)
provide information for how to decode the picture
Sent along with video frame as info packet to inform DSC decoders how to decode the DSC video stream
Target Bpp, Horizontal Slice Count, Vertical Slice Count, Encoded Color Format and Color Depth are all included in PPS along with other parameters
AMD transmits PPS in 2nd line of vblank region

## Slide 6: Forward Error Correction (FEC)
FEC is a technology to reduce the video data errors over DisplayPort cable
DSC achieves compression by referencing adjacent pixels in the same slice. Therefore DSC encoded video frame is sensitive to errors (i.e single pixel error during transmission would cause entire DSC slice to fail)
To solve this problem FEC is designed to work along with DSC to reduce errors
FEC takes a small amount of link bandwidth overhead (2.4% link bandwidth overhead)
DSC Encoding
Original Frame
DSC Encoded
FEC Encoding
DSC with FEC

## Slide 7: SYSTEM REQUIREMENTS

## Slide 8: SYSTEM REQUIREMENTS
Windows OS (7/10)
Navi Family and up
Any Navi supported Display Driver
DSC Capable Display/Hub

## Slide 9: AMD DSC HARDWARE CAPABILITY

## Slide 10: HARDWARE CAPABILITY
Version | DSC 1.1, DSC 1.2a
Video Timing | 480p60Hz – 8K60Hz (total throughput upto 2376 MHz)
Link Rate & Lane Count | RBR – HBR3, 1 – 4 Lanes (DSC can be enabled in any link settings)
Target BPP | 8 bpp – 24 bpp (but limited to 8-16 bpp in current driver)
Minimum Bpp Step | 1/16 bits incremental step
Slice Count | 1 – 8 Horizontal Slices, Arbitrary Vertical Slices

## Slide 11: HARDWARE CAPABILITY
Slice Limitation | Max slice width is 5184 pixels, Min slice height is 8 lines, Max slice throughput is 1188 MHz
Line Buffer Bit Depth | 8 - 13 bits
DSC Encoding Format | RGB, YCbCr 4:4:4, YCbCr 4:2:2 Native, YCbCr 4:2:2 Simple, YCbCr 4:2:0 Native
Source Color Depth | 8 bpc, 10 bpc, 12 bpc

## Slide 12: RX DP DSC CAPABILITY VALIDATION

## Slide 13: Rx DSC Capability Validation
DSC Capabilities (dpcd 0x60) will be used:
DSC SUPPORT
DSC ALGORITHM REVISION
DSC RC BUFFER BLOCK SIZE
DSC SLICE CAPABILITIES 1
DSC LINE BUFFER BIT DEPTH
DSC BLOCK PREDICTION SUPPORT
DSC DECODER COLOR FORMAT CAPABILITIES
DSC DECODER COLOR DEPTH CAPABILITIES
Peak DSC Throughput (both Mode 0 and Mode 1)
DSC Max Slice Width
BITS_PER_PIXEL_INCREMENT
Other Capabilities will be checked:
FEC_CAPABILITY
DPCD_REV
BRANCH OVERALL THROUGHPUT0
BRANCH OVERALL THROUGHPUT1
BRANCH MAX LINKE WIDTH
It is required for RXs to populate correct values accordingly

## Slide 14: AMD DP SST DSC POLICIES
FEC, TARGET BPP, SLICE, PIXEL FORMAT, COLOR DEPTH, BLOCK PREDICTION\LINE BUFFER DEPTH POLICIES

## Slide 15: FEC Policy
FEC will always be enabled on FEC supported RXs for all timings (even for 480p or 2160p@120Hz detail in next slide)
FEC_READY is sent before set mode link training
FEC is enabled after set mode link training (starting from the first video frame)
DSC can only be allowed if FEC is supported
When FEC is supported by a RX, 3% of FEC bandwidth overhead will be deducted from effective link bandwidth.
Effective Link Bandwidth (No FEC support):
Effective Link Bandwidth (FEC support):

## Slide 16: FEC Policy - Examples
Fail Safe Mode @ 1 Lane RBR:
When link training fails completely or EDID read is invalid, fail safe timing 640x480@60Hz 6bit RGB will enabled in 1 lane RBR.
Without FEC support, 37.5% of the effective link bandwidth will be used to enable the fail safe timing.
With FEC support, 38.7% of the effective link bandwidth will be used to enable the same fail safe timing instead due to FEC overhead.
Timings occupying full bandwidth without FEC:
Below timings are supported for given link setting if RX doesn’t report FEC support.
If RX supports FEC, these timings cannot be supported with the given link settings unless DSC is enabled (due to 3% FEC link bandwidth overhead):
  2160p@60 CVT RB 8 bit RGB for 2 lane HBR3
  2160p@120 8 bit RGB for 4 lane HBR3

## Slide 17: Target Bpp Policy
If uncompressed bandwidth of a given timing fits in the max effective link bandwidth of RX, DSC will not be enabled
If max compressed bandwidth of a given timing doesn’t fit in the max effective link bandwidth of RX, the timing will not be enumerated by TX
If a given timing can only fit in the max effective link bandwidth with DSC compression, DSC will be used with the highest target bpp that fits in max effective link bandwidth of RX.
Try to use most of the link bandwidth to allow best image quality

## Slide 18: Target Bpp Policy - Example
Assume Rx supports 4 lane HBR3.
To support 7680x4320@60Hz CVT RB, we could use the lowest 8 target bpp so the bandwidth is sufficient to support this timing.
However our policy will try to use the most of the link bandwidth to allow the best image quality. By applying 8 bit target bpp, we are wasting 1/3 of the link bandwidth.
So instead we will choose 12 bpp based on the outcome of the bandwidth optimization algorithm.
As result, we will drive the same link bandwidth as 8 bpp but with a much better image quality by increasing the target bpp by half.

## Slide 19: Calculate Target Bpp – Internal Only
Variables:
Calculate Target Bpp:
If :
If:
Before DP2.0, target bpp range will be limited to 8-16 bpp to improve interoperability
DPCD 0x6f BITS_PER_PIXEL_INCREMENT field will be taken into account, when determining target bpp
Effective link bandwidth will deduct FEC overhead

## Slide 20: Calculate Target Bpp – Example – Internal Only
Variables:
Calculate Target Bpp:
:
Timing:
7680x4320@60Hz RB1 YCbCr4:4:4 10bpc
Pixel Clock:
2089.75 Mbps
Bpc:
10 bit
PixelFormatFactor:
1
Lane Count:
4 lanes
Link Rate:
8.1 GHz
8b10b Overhead:
20%
Min bpp:
8 bpp
Max bpp:
16 bpp
Bpp step:
1/16 bpp

## Slide 21: Slice Policy
Reduce RX’s slice resources, restrict error propagation
Minimum number of horizontal slices that can fit in RX’s slice throughput is preferred
The selected number of horizontal slices has to be divisible by timing’s h total
Maximum number of vertical slices that RX can support is preferred
The selected number of vertical slices has to be divisible by timing’s v total
For YCbCr 4:2:2 native and YCbCr4:2:0 native, value from DPCD 0x6B Throughput Mode 1 will be taken into account
For other pixel formats, value from DPCD 0x6B Throughput Mode 0 will be taken into account

## Slide 22: DSC Encoding Format Policy
Only support a DSC Encoding Format if the RX supports the format both in the EDID and DSC capability
Only use simple format when native format is not supported
DSC Encoding Format\ Uncompressed Pixel Format | RGB | YCbCr 4:4:4 | YCbCr 4:2:2 | YCbCr 4:2:0
DSC RGB | Supported and Default |  |  | 
DSC YCbCr 4:4:4 |  | Supported |  | 
DSC YCbCr 4:2:2 Simple |  |  | Supported (if DSC YCbCr 4:2:2 Native not supported) | 
DSC YCbCr 4:2:2 Native |  |  | Supported | 
DSC YCbCr 4:2:0 Native |  |  |  | Supported

## Slide 23: Uncompressed Color Format Enumeration Requirements (for DisplayPort)
Source Pixel Encoding | Condition | Supported Timings
RGB | N/A | All
YCbCr 4:4:4 | EDID1.4 block -> EDID Basic Parameters -> Color Type is 1 (RGB 4:4:4 & YCbCr 4:4:4) or 3 (RGB 4:4:4 & YCbCr 4:4:4 & YCbCr 4:2:2) | All
 | CTA Ext block -> General Info -> YCbCr 4:4:4 support is 1 | All
 | DisplayID -> DisplayInterface Block ->YCbCr 4:4:4 Color Depth supports (based on individual color depths) | All timings with reported color depths
YCbCr 4:2:2 | EDID1.4 block -> EDID Basic Parameters -> Color Type is 2 (RGB 4:4:4 & YCbCr 4:2:2) or 3 (RGB 4:4:4 & YCbCr 4:4:4 & YCbCr 4:2:2) | All
 | CTA Ext block -> General Info -> YCbCr 4:2:2 support is 1 | All
 | DisplayID -> DisplayInterface Block -> YCbCr 4:2:2 Color Depth supports based on individual color depths | All timings with reported color depths
YCbCr 4:2:0 | CTA Ext block -> YCbCr 4:2:0 Video Data Block or YCbCr 4:2:0 Capability Map Data Block based on individual timings | Reported Timings
 | DisplayID -> DisplayInterface Block -> YCbCr 4:2:0 Color Depth supports based on individual color depths | All timings with reported color depths

## Slide 24: Color Depth Policy
Only support a DSC color depth if the RX supports the color depth both in the EDID and DSC capability
DSC Color Depth\ Uncompressed Color Depth | 6 bit | 8 bit | 10 bit | 12 bit
DSC 8 bit |  | Supported |  | 
DSC 10 bit |  |  | Supported and Preferred | 
DSC 12 bit |  |  |  | Supported

## Slide 25: Block Prediction/Line Buffer Bit Depth Policy
Block Prediction
Source TX will always enable DSC block prediction as long as RX’s DSC BLOCK PREDICTION SUPPORT (dpcd 0x66) bit 0 is set to 1
Line Buffer Bit Depth
Source TX will use the minimum between source max DSC line buffer bit depth (13 bit) and parsed value from RX’s DSC LINE BUFFER BIT DEPTH (dpcd 0x65)

## Slide 26: AMD DP SST DSC ENABLEMENT SEQUENCE

## Slide 27: Display Hotplug
Hotplug Detection
Mode Enumeration/ Query
Set Mode (enable)
  FEC READY = 1
  Link Training
  Send Idle Pattern
  DSC EANBLE = 1
  PPS/FEC/DSC enabled in First Video Frame

## Slide 28: Display Disable
Set Mode (disable display)
  Send Idle Pattern
  Disable DP Link
  FEC READY = 0
  DSC ENABLE = 0

## Slide 29: Display Mode Change
Set Mode (Mode Change)
  Send Idle Pattern
  Disable DP Link
  FEC READY = 0
  DSC ENABLE = 0
  FEC READY = 1
  Set Mode Link Training
  Send Idle Pattern
  DSC ENABLE = 1
  PPS/DSC/FEC enabled in First Video Frame

## Slide 30: Dynamic Target Bpp update
According to DP 1.4a specs 2.7.3.3 once DSC_ENABLE is set to 1, RX shall:
Read the first PPS values
Enable decompression when CompressedStream_Flag is set to 1 in VB-ID bit 6 with the last PPS values received
Apply new PPS values on next frame when new PPS values are received
Disable decompression when VB-ID bit 6 is set to 0

## Slide 31: AMDDSAT DSC TOOL

## Slide 32: AMDDSAT DSC TOOL (Starting From 2.3.7)

## Slide 33: AMDDSAT DSC TOOL – Internal Only

## Slide 34: AMD DP SST DSC TEST PLAN

## Slide 35: DP SST DSC Test Plan
Factors need to be tested:
Lane Count and Link Rate
  1-4 lanes, RBR-HBR3
Color Format and Color Depth
  8-12 bpc,
  RGB, YCbCr 4:4:4, YCbCr 4:2:2 Simple/Native, YCbCr 4:2:0 Native
Interoperability
  with other features (ex. FreeSync, HDR, HDCP, etc)
  with common use cases (ex. system sleep, boot up, driver PnP, etc)

## Slide 36: SST DSC Link Rate and Lane Count Test Plan
Link Rate | Lane Count | Timing | Pixel Encoding | bpc
HBR3 | 4 | 7680x4320@60Hz CVT RB2 | RGB 4:4:4 | 10
HBR3 | 4 | 7680x4320@60Hz CVT BR1 | RGB 4:4:4 | 10
HBR3 | 4 | 7680x4320@60Hz CTA | YCbCr 4:4:4 | 10
HBR3 | 4 | 3840x2160@144Hz CVT RB1 | RGB 4:4:4 | 10
HBR3 | 4 | 5120x2880@60Hz | RGB 4:4:4 | 10
HBR3 | 4 | 3840x2160@120Hz | RGB 4:4:4 | 10
HBR3 | 2 | 5120x2880@60Hz | RGB 4:4:4 | 10
HBR3 | 2 | 3840x2160@60Hz CTA | RGB 4:4:4 | 10
HBR2 | 2 | 3840x2160@60Hz CVT RB1 | RGB 4:4:4 | 10
RBR | 1 | 1920x1080@60Hz CTA | YCbCr 4:4:4 | 10

## Slide 37: Pixel Format and Color Depth Test Plan
Timing | Pixel Encoding | Color Depth | Lane Count | Link Rate
3840x2160@144Hz CVT RB2 | YCbCr 4:4:4 | 8 bit | 4 | HBR3
3840x2160@144Hz CVT RB2 | YCbCr 4:4:4 | 10 bit | 4 | HBR3
3840x2160@144Hz CVT RB2 | YCbCr 4:4:4 | 12 bit | 4 | HBR3
3840x2160@144Hz CVT RB2 | RGB 4:4:4 | 8 bit | 4 | HBR3
3840x2160@144Hz CVT RB2 | RGB 4:4:4 | 10 bit | 4 | HBR3
3840x2160@144Hz CVT RB2 | RGB 4:4:4 | 12 bit | 4 | HBR3
3840x2160@144Hz CVT RB2 | YCbCr 4:2:2 | 8 bit | 4 | HBR3
3840x2160@144Hz CVT RB2 | YCbCr 4:2:2 | 10 bit | 4 | HBR3
3840x2160@144Hz CVT RB2 | YCbCr 4:2:2 | 12 bit | 4 | HBR3
3840x2160@144Hz CVT RB2 | YCbCr 4:2:0 | 8 bit | 2 | HBR3

## Slide 38: VIRTUAL DP PEER DEVICE OVERVIEW

## Slide 39: Types of Virtual DP Peer Device
Virtual DP Sink Peer Device (MST Display) RX DPCD from RAD 0 Virtual DPCD from RAD 0.8
Virtual DP to HDMI Protocol Converter Peer Device (HDMI output after MST hub) RX DPCD Not Present Virtual DPCD from RAD 0.1
Virtual DP to DP peer Device (DP output after MST hub) RX DPCD from RAD 0.2.1 Virtual DPCD from RAD 0.2

## Slide 40: AMD VIRTUAL DP DEVICE ENUMERATION

## Slide 41: Virtual DP Sink Peer Device Enumeration
Virtual DP Sink Peer Device Enumeration:
Virtual DPCD port is logical port (port 8-15)
Port Info for the logical port needs:
  DPCD_Revision >= 1.4
D

## Slide 42: Virtual DP to HDMI Protocol Converter Peer Device Enumeration
Virtual DP to HDMI Protocol Converter Peer Device Enumeration:
Port Info for virtual DPCD port needs :
  Peer_Device_Type = 4
  Messaging_Capability_Status = 0
  Legacy_Device_Plug_Status = 1
  DPCD_Revision >= 1.4

## Slide 43: Virtual DP to DP Peer Device Enumeration
Virtual DP to DP Peer Device Enumeration:
Port Info for virtual DPCD port needs:
  Peer_Device_Type = 2
  DPCD_Revision >= 1.4
Virtual DPCD Peer Device has only 1 output port
Virtual DPCD Peer Device output port has Peer_Device_Type = 1

## Slide 44: Virtual DP to DP Peer Device with Virtual DPCD on Disconnection
When Downstream DP display is disconnected from the downstream facing DP++ Connector,
MST hub needs alter its topology so that the virtual DP to DP peer device is no longer present.

## Slide 45: Virtual DP to DP Peer Device with Virtual DPCD MST Connection
When downstream facing DP++ Connector is connected to MST Topology,
MST hub needs alter its topology so that the virtual DP to DP peer device is no longer present.

## Slide 46: AMD DP MST DSC POLICY OVERVIEW

## Slide 47: AMD MST DSC Policy Overview
FEC | Shared with DP SST
TARGET BPP | Not shared with DP SST, will cover in later slide
SLICE | Shared with DP SST
PIXEL FORMAT | Shared with DP SST
DSC DECODING SELECTION | Not shared with DP SST, will cover in later slide
MST DSC has its own Target bpp and DSC encoding selection policies

## Slide 48: AMD MST DSC DECODING SELECTION POLICY

## Slide 49: AMD MST DSC Decoding Selection Policy
Given a discovered sink device and a MST topology, Source TX needs to determine following two items:
  If DSC decoding is supported
  Whether to enable DSC decoding on RX side or Virtual DP peer device side
Based on AMD FEC Policy, DSC is only allowed if FEC is supported. Therefore Source TX will check
  FEC Capability (0x130) from the immediate MST branch device
  FEC_Capability field in PATH_ENUM_RESOURCE equal to 1 for each MST branch device along the path to the RX port. (with exception of virtual DP peer device as it is connected internally)
For virtual DP to DP peer device, source TX prefers DSC decoding on RX side if:
  FEC_Capability is equal to 1 for the RX port
  And the sink RX device supports FEC and DSC
  And the virtual DPCP reports MST to SST DSC passthrough support (0x60 bit 1)
For other types of virtual DP peer device or the virtual DP to DP peer device not fulfilling above conditions, source TX will select DSC decoding on virtual DP peer device side if:
  DSC capability reported from virtual DPCD is valid

## Slide 50: AMD MST DSC Decoding Selection Policy Diagram
FEC has to be supported in red
virtual DPCD has to be enumerated in red
If below conditions are true, enable DSC on RX side
  DSC MST to SST passthrough is supported in yellow
  DSC/FEC is supported in yellow
Otherwise if below conditions are true, enable DSC on Virtual DPCD side:
  DSC is supported in green

## Slide 51: AMD MST BANDWIDTH VALIDATION WITH DSC

## Slide 52: Types of Bandwidth Validation
Link Bandwidth Validation Validate bandwidth for the immediate downstream MST branch Device
Topology Bandwidth Validation Validate bandwidth for each MST branch device connected after the immediate MST branch Device
Endpoint Bandwidth Validation Validate bandwidth for the sink device connected at the endpoint of the MST topology

## Slide 53: MST Link Bandwidth Validation – Internal Only
is an arbitrary unit chosen to represent MST bandwidth. The unit is defined below:
then could be calculated by:
When converting to a 0.6% margin needs to be included:
So should be:
MST has in total of non-MTPH time slots available.
Therefore, MST link bandwidth is validated if:
Link Bandwidth Validation can be expressed as a function operating on a set of timing bandwidths:

## Slide 54: MST Topology Bandwidth Validation - Internal Only
ENUM_PATH_RESOURCE will be issued to each MST Branch Device
In ENUM_PATH_RESOURCE message, Full_Payload_Bandwidth_Number () and FEC_Capability will be recorded
If FEC_Capability is set to 1, it means FEC will be enabled, so a 3% FEC overhead will be deducted in
That is:
  If FEC_Capability is 1:
  Else:
Then for each MST Branch Device, calculate the required PBN:
  Assume there are downstream timings numbered , then:
If every MST Branch Device can fulfil below condition:
  Then MST Topology Bandwidth is validated
Topology Bandwidth Validation can be expressed as a function operating on a set of timing bandwidths:

## Slide 55: MST Endpoint Bandwidth Validation - Internal Only
ENUM_PATH_RESOURCE will be issued to each connected down facing endpoint port
In ENUM_PATH_RESOURCE message, Full_Payload_Bandwidth_Number () and FEC_Capability will be recorded
If FEC_Capability is set to 1, it means FEC will be enabled, so a 3% FEC overhead will be deducted in
That is:
  If FEC_Capability is 1:
  Else:
For each endpoint down facing port, decide if DSC should be decoded on RX side (logic will be covered in AMD MST DSC Decoding Policy)
If DSC decode on RX side is needed:
Else:
For each endpoint down facing port, If endpoint down facing port can fulfil below condition:
  Then MST Endpoint Bandwidth is validated
Endpoint Bandwidth Validation can be expressed as a function operating on a set of timing bandwidths:

## Slide 56: AMD MST DSC TARGET BPP POLICY

## Slide 57: AMD Target Bpp Policy for MST Topology Overview
Try to apply AMD DSC bandwidth optimization and elimination algorithm to streams so that the link bandwidth could be utilized to its maximum potential
Apply Minimum Target BPP
For MST Topology
Apply Target BPP Optimization Algorithm For MST Topology
Apply DSC Compression Elimination Algorithm For MST Topology
Enable Optimized Target BPP Solution For MST Topology

## Slide 58: AMD Target Bpp Optimization Example
4K60Hz CVT RB RGB 10bit
Display 1
Display 2
Apply Target BPP Optimization Algorithm For MST Topology
4K60Hz CVT RB RGB 10bit
Display 1
Display 2
4K60Hz CVT RB RGB 10bits
DSC@11 4/16 bpp
(31 Time Slots)
DSC@11 10/16 bpp
(32 Time Slots)
4K60Hz CVT RB RGB 10bit
2 Lane HBR3 Link Bandwidth

## Slide 59: AMD Target Bpp Optimization Example
1440p@60Hz RGB 10 bit
Display 1
Display 2
Apply DSC Compression Elimination Algorithm For MST Topology
Display 1
Display 2
No DSC Required
(36 Time Slots)
DSC@16 bpp
(20 Time Slots)
1440p@60Hz RGB 10 bit
2 Lane HBR3 Link Bandwidth
1440p@60Hz RGB 10 bit
1440p@60Hz RGB 10 bit

## Slide 60: AMD Target Bpp Policy Overview - Internal Only
Validate with No DSC Compression
Validate with Maximum DSC Compression
Validate with Minimum DSC Compression
DSC Optimization Algorithm
DSC Elimination Algorithm
Try to “fairly” distribute bandwidths among DSC capable streams to fully utilize link bandwidth

## Slide 61: MST DSC No/Maximum/Minimum Compression Validation - Internal Only
Timing Bandwidth Set with No DSC Compression:
Timing Bandwidth Set with Max DSC Compression:
Timing Bandwidth Set with Min DSC Compression:
Link Validation:
Topology Validation:
Endpoint Validation:

## Slide 62: MST DSC Compression Optimization Algorithm - Internal Only
MST DSC Compression Optimization Algorithm will be used when Maximum Compression Validation passes but Minimum Compression Validation fails.
In this scenario, there is a scarce bandwidth resource with Capacity () needed to be fairly distributed among resource demands sorted in increasing order. i.e.
could be represented by the remaining time slots after all streams have been allocated with maximum compression timing bandwidth:
Resource demands could be represented by PBN required to upgrade a timing from maximum compression to minimum compression:
Then define below:
*
Finally the logic goes below:
  for i in 1...n:
  if x[i] <= AvgShare:
  pbn[i] = pbn_with_max_target_bpp[i]
  else
  pbn[i] = pbn_with_min_target_bpp + AvgShare
  if validate_link(pbn) && validate_topology(pbn) && validate_endpoint(pbn):
  target_bpp[i] = calculate_target_bpp(pbn[i])
  AvgShare = calculate_avgshare_with_remaing_streams(pbn, n-1)
  else
  target_bpp[i] = MinTargetBpp
  break
Below formula will be used to calculate from a give :

## Slide 63: MST DSC Compression Elimination - Internal Only
MST DSC Compression Elimination Algorithm will be used when Minimum Compression Validation passes but No DSC Compression Bandwidth Validation fails.
In this scenario, first compute and sort the resource demands in increasing order. i.e.
However unlike Compression Optimization Algorithm, we could either enable DSC compression or disable DSC compression. In other words demands could be either fulfilled or not fulfilled.
So the logic goes below:
  for i in 1...n:
  pbn[i] = pbn_with_max_target_bpp[i] + x[i]
  if validate_link(pbn) && validate_topology(pbn) && validate_endpoint(pbn):
  dsc_enble[i]= false
  else
  break

## Slide 64: AMD DP MST DSC ENABLEMENT SEQUENCE

## Slide 65: Hotplug to Hub RX (2 displays)
Hotplug Detection/Topology Discovery
Mode Enumeration/Query/ Cofunctional Validation
Set Mode (enable)
  FEC READY = 1
  Link Training
  Send Idle Pattern
  Update VC Payload Table (VC1)
  Write Remote DSC ENABLE (VC1)
  FEC/DSC/PPS enable in First Video Frame
  Send Idle Pattern
  Update VC Payload Table (VC1, VC2)
  Write Remote DSC ENABLE (VC2)
  FEC/DSC/PPS enable in First Video Frame

## Slide 66: Disable All Streams in Existing Topology
User puts System into Sleep
Disable VC1 but keeps the link on
  Send Idle Pattern
  Update Payload VC Table
  Write DSC_ENABLE to 0
Disable VC2 and turn off the link
  Update Payload VC Table
  Write DSC_ENABLE to 0
  Disable DP link
  Set FEC READY (0x120) to 0

## Slide 67: Enable Stream in Existing Topology
User enables VC1
Mode Enumeration/ Query/Cofunctionality Validation
Set Mode (enable VC1)
  Send Idle Pattern
  Update VC Payload Table
  Allocation Payload Remote Message
  Write DSC ENABLE to Selected Port
  FEC/DSC/PPS enable in First Video Frame

## Slide 68: Disable Stream in Existing Topology
User disables VC1
Mode Enumeration/ Query/Cofunctionality Validation
Set Mode (disable VC1)
  Send Idle Pattern
  Update VC Payload Table
  Allocation Payload Remote Message
  Write DSC ENABLE to 0 to Selected Port
  Disable Idle Pattern

## Slide 69: Mode Change in Existing Topology
User change mode for VC1
Mode Enumeration/ Query/Cofunctionality Validation
Set Mode (mode change VC1)
  Send Idle Pattern
  Update VC Payload Table
  Allocation Payload Remote Message to 0
  Write DSC ENABLE to 0 to Selected Port
  Update VC Payload Table
  Allocate Payload Remote Message
  Write DSC_ENABLE to 1 to Selected Port
  FEC/DSC/PPS enable in First Video Frame

## Slide 70: MST DSC Seamless Target Bpp Update Sequence
AMD is proposing a seamless dynamics target bpp update sequence on existing streams
The sequence requires MST branches to support to seamlessly update VC payload allocation along with target bpp update

## Slide 71: MST DSC Sequence for Reducing Payload
Sequence for reducing payload:
Recude Throttled_VCP_Size
Send ALLOCATE_PAYLOAD on existing stream with new pbn
Update VC Payload ID Table

## Slide 72: MST DSC Sequence for Increasing Payload
Sequence for increasing payload:
Send ALLOCATE_PAYLOAD on existing stream with new pbn
Update VC Payload ID Table
Recude Throttled_VCP_Size

## Slide 73: AMD DP MST DSC TEST PLAN

## Slide 74: MST DSC Test Plan Overview
Factors need to be tested (addition to SST Test Plan):
Lane Count and Link Rate
  1-4 lanes, RBR-HBR3
Interoperability
  with other features (ex. FreeSync, HDR, HDCP, etc)
  with common use cases (ex. system sleep, boot up, driver PnP, etc)

## Slide 75: MST DSC Link Rate and Lane Count Test Plan
Lane Count | Link Rate | Display 1 | Display 2 | Display 3
4 | HBR3 | 3840x2160@60Hz CVT RB1 | 3840x2160@60Hz CVT RB1 | 3840x2160@60Hz CVT RB1
4 | HBR3 | 3840x2160@60Hz CVT RB1 | 3840x2160@60Hz CVT RB1 | 1920x1080@60Hz CTA(Uncompressed)
2 | HBR3 | 3840x2160@60Hz CVT RB1 | 3840x2160@60Hz CVT RB1 | N/A
2 | HBR3 | 2560x1440@60Hz RB1 | 2560x1440@60Hz RB1 | 2560x1440@60Hz RB1
4 | HBR2 | 3840x2160@60Hz CVT RB1 | 3840x2160@60Hz CVT RB1 | N/A
4 | HBR2 | 2560x1440@60Hz RB1 | 2560x1440@60Hz RB1 | 2560x1440@60Hz RB1
2 | HBR2 | 3840x2160@60Hz CVT RB1 | N/A | N/A
4 | HBR3 | 7680x4320@60Hz CVT RB1 | N/A | N/A
4 | HBR3 | 7680x4320@60Hz CVT RB2 | 1920x1080@60Hz CTA(Uncompressed) | N/A
4 | HBR3 | 7680x4320@30Hz | 7680x4320@30Hz | N/A

## Slide 76: AMD DEBUG LOG – Internal Only

## Slide 77: DSC SOFTWARE DESIGN OVERVIEW

## Slide 78: DSC Software Design Overview

## Slide 79: DSC Config

## Slide 80: Q&A